CS3514 Laboratory Session:

Name:	Nathan Crowley

Student ID:	118429092

Repeat the following sections for each question

Answer:
I started by setting all of Port D’s pins to low (0-7) with DDRD. Then I set the RED led as pin 9 and the GREEN led as pin8. I then loop through each of PORT D’s pins, and check if adjacent pins (i and i+1) are either both HIGH or both LOW. Setting red and green led on accordinlying with digitalWrite().

Code:
/*PORT D = pins 0 to 7
 *
 *TASK:
 *Wrtie a program that simultaneously read the values of Port D.
 * - turn on Red LED if any two adjacent pins are HIGH
 * - turn on Green LED if any two adjacent pins are LOW
 *
 * NOTE: you can connect the Port D pins to +5v or 0v with wires. As you change the connections,
 * your program should illuminate the LEDs appropriately.
 *
 * SOLUTION: Pins - 01234567
 * two adjacent pins HIGH would be = 00011000
 * two adjacent pins HIGH would be = 11100111
 * set PORT D as all outputs.
 * Loop through Port D and check if two adjacent pins (i and i+1) are either HIGH or LOW
 * Turn on red if both high
 * turn on green ifboth low

 */
int LED_RED = 9;
int LED_GREEN = 8;

void setup() {
  // 0 = input 1 = output
  DDRD = B00000000;
}

void loop() {
        //76543210
    for(int i=0; i<7;i++){
      if(digitalRead(i)==HIGH && digitalRead(i+1)==HIGH){
        digitalWrite(LED_GREEN,LOW);
        digitalWrite(LED_RED,HIGH);
      }
      else if(digitalRead(i)==LOW && digitalRead(i+1)==LOW){
        digitalWrite(LED_RED,LOW);
        digitalWrite(LED_GREEN,HIGH);
      }
    }
    delay(1000);
}
Photos:
-two adjaceny HIGH	-two adjacent LOW